## Slide 1
Material Library
Imperial units
The RISA-3D material tables as the reference for Python Solver Rev.2
Eight material tabs, 41 materials, one masonry self-weight rule, in kip, inch, foot and °F as RISA displays them. What every column means, how the numbers were derived, and how the solver should consume them.
Mark Airol Escranda | Numerical Methods, Lab 03 | September 2026
Notes: Source: nine screenshots in the Materials folder. Companion workbook: RISA_Materials_Library_Imperial.xlsx.

## Slide 2
Where material properties enter the solver
Python Solver Rev.2 | Material Library, Imperial | 2
A stiffness solver never uses a material name. It uses four numbers, and a fifth for loads. Everything on the eight RISA tabs exists to supply these.
E
Modulus of elasticity
Axial term EA/L and bending terms 12EI/L³, 6EI/L², 4EI/L in the member stiffness matrix. Also plate membrane stiffness.
G
Shear modulus
Torsional stiffness GJ/L, and the shear-deformation correction on deep members. Isotropic rule: G = E / 2(1+ν).
ν
Poisson's ratio
Links G to E and sets the in-plane coupling of plate and shell elements.
γ
Unit weight
Self-weight load: w = γ · A per unit length. Converted to nodal forces in the load vector.
α
Thermal coefficient
Thermal strain α·ΔT, turned into equivalent member end forces for temperature load cases.
Strengths (Fy, Fu, f'c, f'm, Ftu) do not change the stiffness solution. They belong to the design-check layer that sits on top of the analysis.

## Slide 3
The library at a glance
Python Solver Rev.2 | Material Library, Imperial | 3
8
material tabs in RISA-3D
41
materials transcribed
5
stiffness properties shared by every tab
Tab | Rows | What it holds | Extra columns beyond the shared five
Hot Rolled | 5 | A36, A572, A992, A500 steels | Yield, Fu, Ry, Rt
Cold Formed | 2 | A570_33, A607_C1_55 | Yield, Fu
Wood | 12 | Solid sawn, glulam, LVL | Type, Database, Species, Grade, Cm, Ci, Emod
Concrete | 6 | 3 to 4 ksi, normal and lightweight | f'c, Lambda, Flex Steel, Shear Steel
Masonry | 2 | Concrete and clay masonry | f'm, Flex Steel, Shear Steel, Self Weight rule
Aluminum | 6 | 3003, 5052, 6061, 6063 alloys | Table B.4, kt, Ftu, Fty, Fcy, Fsu, Ct
Stainless | 1 | SS1 | n (Ramberg-Osgood), Yield, Fu
General | 7 | Generic concrete, aluminum, steel, RIGID | Plate Methodology

## Slide 4
The five shared columns, and their units
Python Solver Rev.2 | Material Library, Imperial | 4
Column | Unit | Meaning | Solver note
E [ksi] | kip/in² | Modulus of elasticity | 1 ksi = 6.894757 MPa. Steel 29,000 ksi = 199,948 MPa.
G [ksi] | kip/in² | Shear modulus | Derive from E and ν when blank; tabulated G agrees within 0.1% on 22 of 28 rows.
Nu | dimensionless | Poisson's ratio | Steel 0.30, concrete 0.15, masonry 0.25, aluminum 0.33, wood 0.30.
Therm. Coeff. [1e-5/°F] | 10⁻⁵ per °F | Coefficient of thermal expansion | Multiply by 1e-5 first: steel 0.65 → 6.5e-6 /°F = 11.7e-6 /°C.
Density [k/ft³] | kip/ft³ | Unit weight for self-weight | 1 k/ft³ = 157.09 kN/m³. Steel 0.49 k/ft³ = 490 pcf = 77.0 kN/m³.
Unit strategy for the solver
Store the library exactly as RISA shows it (kip, inch, foot, °F) and convert once at the boundary. The companion Metric library carries the same 41 rows converted with 1 ksi = 6.894757 MPa, 1 k/ft³ = 157.0875 kN/m³, 1e-5/°F = 18 × 1e-6/°C.
A mixed-unit row is the classic silent error; the Stainless tab shows what that looks like.
Consistency check built into the workbook
Every tab with a G column carries a formula column: G_calc = E / 2(1+ν), and the percentage difference from the tabulated G.
22 of the 28 rows with a G value agree within 0.1%. The six aluminum rows carry a fixed 3,787.5 ksi, which is 3E/8 with E = 10,100 (ν = 1/3 exactly), so they sit 0.25% off, and 1.2% off for 5052 with its E of 10,200.

## Slide 5
Hot Rolled steel
Python Solver Rev.2 | Material Library, Imperial | 5
Materials-SS-Hot-Rolled-TAB.png
Five ASTM grades. Stiffness is identical across all of them: E = 29,000 ksi, G = 11,154 ksi, ν = 0.30, γ = 0.49 k/ft³.
Only the strength columns differ. A36 yields at 36 ksi; A572 Gr.50 and A992 at 50 ksi; A500 tube steels at 42 and 46 ksi. Fu is 58 ksi throughout.
Ry and Rt are the AISC 341 expected-strength ratios. Ry × Fy is the expected yield (A36: 1.5 × 36 = 54 ksi), used when a seismic design must guarantee that a brace or link yields before its connection.
For the solver: one stiffness set, five design labels. The material dictionary can share E, G, ν and vary only Fy, Fu, Ry, Rt.
Unit weight check
0.49 k/ft³ × 1000 = 490 pcf, the standard unit weight of structural steel. A W12×26 (A = 7.65 in²) weighs 490 × 7.65/144 = 26.0 lb/ft, matching its designation.

## Slide 6
Cold Formed steel
Python Solver Rev.2 | Material Library, Imperial | 6
Materials-SS-Cold-Formed-TAB.png
Two sheet-steel grades used for light-gauge framing: A570 Gr.33 (Fy 33, Fu 52 ksi) and A607 Class 1 Gr.55 (Fy 55, Fu 70 ksi).
Note the different modulus: E = 29,500 ksi, not 29,000. AISI S100 specifies 29,500 ksi for cold-formed members, and G = 11,346 ksi follows from E / 2(1.3).
No Ry or Rt columns. Cold-formed design under AISI does not use the AISC expected-strength factors.
For the solver: keep this tab separate from Hot Rolled even though the numbers look alike. A 1.7% difference in E is real and shows up in deflections.
Why 29,500 matters
Deflection is proportional to 1/E, so swapping in 29,000 ksi overstates cold-formed deflection by 1.7%. Small, but it is the kind of drift that makes a solver disagree with RISA on a benchmark.

## Slide 7
Concrete
Python Solver Rev.2 | Material Library, Imperial | 7
Materials-SS-Concrete-TAB.png
Six mixes: 3,000, 3,500 and 4,000 psi, each in normal weight (145 pcf, λ = 1.0) and lightweight (110 pcf, λ = 0.75).
E is not typed in; it is derived from f'c and unit weight with ACI 318 Eq. 19.2.2.1(a): Ec = wc¹·⁵ · 33 · √f'c (psi).
Check: 145¹·⁵ × 33 × √3000 = 3,156,000 psi = 3,156 ksi, exactly the Conc3000NW value. For 110 pcf: 2,085 ksi, matching Conc3000LW.
ν = 0.15 for all mixes, so G = E / 2.3. Flex Steel and Shear Steel (60 ksi) are the Grade 60 rebar yield used by the design layer only.
Rule for the solver
Store f'c and γ as the inputs and compute E on load: E_ksi = (γ_pcf)^1.5 × 33 × √(f'c_psi) / 1000. That reproduces every RISA value to the nearest ksi and keeps custom mixes consistent.

## Slide 8
Masonry, and how its self-weight is computed
Python Solver Rev.2 | Material Library, Imperial | 8
Materials-SS-Masonry-TAB.png
Masonry-Self-Weight-WND.png
Self Weight = Custom
The tab does not carry a density. Instead the dialog selects "Using Block and Grout Properties": block material Conc 115 pcf, grout 140 pcf.
Wall weight then depends on block thickness and grout spacing. The greyed-out alternative is a uniform 0.08 k/ft³ (80 pcf).
Two assemblies: concrete masonry (E 1,350 ksi) and clay masonry (E 1,050 ksi), both with f'm = 1.5 ksi and ν = 0.25.
E follows TMS 402: Em = 900 f'm for concrete masonry (900 × 1.5 = 1,350) and 700 f'm for clay (700 × 1.5 = 1,050). G = 0.4 Em = 540 and 420 ksi, which also equals E / 2(1.25).
For the solver: masonry needs a wall-panel weight routine, not a scalar density. Simplest faithful implementation: weight per area = f(block thickness, block density, grout density, grout spacing) from the NCMA tables, with 80 pcf as the fallback.

## Slide 9
Wood
Python Solver Rev.2 | Material Library, Imperial | 9
Materials-SS-Wood-TAB.png (labels in rows 7 to 12 truncated on screen; reconstructed from Species)
Twelve entries in three families: six visually graded solid-sawn species (No.1), four 24F-1.8E glulam layups from NDS Table 5A (balanced and unbalanced, DF and SP), and two custom LVL products (1.5E-2250F, 2.0E-2900F).
This tab stores keys, not stiffness. E, Fb, Fv and Fc are looked up in the NDS Supplement by Type, Database, Species and Grade; Emod (1.0) scales the tabulated E, and Cm / Ci apply wet-service and incising factors when checked (none are).
Shared values: ν = 0.30, α = 0.3 × 1e-5 /°F, γ = 0.035 k/ft³ (35 pcf).
For the solver: wood needs a lookup layer. Until the NDS table is loaded, a placeholder E (for example 1,700 ksi for No.1 DF-L) keeps the model solvable.
The glulam label decoded
24F-1.8E: allowable bending stress 2,400 psi and E = 1.8 × 10⁶ psi = 1,800 ksi. BAL and UNBAL mark balanced or unbalanced layups; DF and SP are Douglas Fir and Southern Pine laminations.

## Slide 10
Aluminum
Python Solver Rev.2 | Material Library, Imperial | 10
Materials-SS-Aluminum-TAB.png (row 6 truncated on screen; strengths match welded 6061-T6)
Six alloy-tempers: 3003-H14, 5052-H34, 6061-T6 (plain and welded), 6063-T5 and 6063-T6.
Stiffness is nearly constant: E = 10,100 ksi (10,200 for 5052), G = 3,787.5 ksi for every row (3E/8, the ADM value for ν = 1/3), ν = 0.33, γ = 0.173 k/ft³ (173 pcf), α = 1.3 × 1e-5 /°F, twice that of steel.
Strength columns follow the Aluminum Design Manual: Ftu, Fty (tension), Fcy (compression), Fsu (shear), with kt = 1.0 and the buckling constants taken from Table B.4-1 or B.4-2 depending on temper. Ct = 141 is the compression constant.
Welding halves the strength but not the stiffness: 6061-T6 drops from Fty 35 to 15 ksi in the welded row while E stays at 10,100 ksi.
Thermal note for the solver
Aluminum expands at 13.0e-6 /°F versus 6.5e-6 for steel. A 40 ft aluminum member under a 60 °F rise grows 0.37 in; the same steel member grows 0.19 in. Thermal load cases must read α per material, not a global constant.

## Slide 11
Stainless: one row, and a unit trap
Python Solver Rev.2 | Material Library, Imperial | 11
Materials-SS-Stainless-TAB.png
Column | Displayed in RISA | If read as ksi | If read as MPa
E | 1.931e+5 | 193,100 ksi (6.7× steel) | 193,100 MPa = 28,000 ksi
Yield | 206.843 | 206.8 ksi | 206.843 MPa = 30.0 ksi
Fu | 517.107 | 517.1 ksi | 517.107 MPa = 75.0 ksi
Density | 8.009 | 8,009 pcf | 8.0 g/cm³ (specific gravity of stainless)
SS1 is the only stainless entry. Its values sit under ksi headers but are SI magnitudes: 30 ksi yield and 75 ksi ultimate are the textbook Type 304 values, and 193 GPa is its modulus.
n = 5.6 is the Ramberg-Osgood exponent, the one property unique to this tab. Stainless has no sharp yield, so RISA models the stress-strain curve as ε = σ/E + 0.002 (σ/Fy)ⁿ.
Treat this row as a caution, not a value. Either RISA's unit setting changed while the row was entered, or the row was pasted from an SI source. Confirm before the solver uses it.
The workbook records the row as displayed and flags it on the Stainless and All Materials sheets.

## Slide 12
General materials and the RIGID link
Python Solver Rev.2 | Material Library, Imperial | 12
Materials-SS-General-TAB.png
Seven generic entries for plates, solids and quick models: four concretes (3 and 4 ksi, normal and lightweight), one aluminum, one steel, and RIGID.
gen_Conc3NW (E 3,155) and gen_Conc4NW (E 3,644) mirror the Concrete tab values within 1 ksi; gen_Alum uses E 10,600 ksi and α 1.29, slightly different from the Aluminum tab.
Plate Methodology = Isotropic for every entry: the same E in every in-plane direction, which is what the solver's plate stiffness should assume.
RIGID has E = 1e+6 ksi, no G, and zero density and thermal coefficient. It is a modeling device for stiff links and rigid offsets, not a real material.
Handling RIGID in the solver
Do not simply use E = 1e6 in the stiffness matrix; a 34:1 stiffness ratio to steel is fine, but combine it with tiny members and the matrix becomes ill-conditioned. Better: implement rigid links as constraint equations, or cap E at 1,000× the stiffest real material.

## Slide 13
How Solver Rev.2 should consume the library
Python Solver Rev.2 | Material Library, Imperial | 13
from dataclasses import dataclass
import pandas as pd
@dataclass
class Material:
label: str; category: str
E: float; nu: float; density: float
alpha: float; G: float | None = None
Fy: float | None = None; Fu: float | None = None
def __post_init__(self):
if self.G is None: # isotropic rule
self.G = self.E / (2 * (1 + self.nu))
self.alpha *= 1e-5 # RISA stores 1e-5/degF
df = pd.read_excel('RISA_Materials_Library_Imperial.xlsx',
sheet_name='All Materials', header=3)
LIB = {r['Label']: Material(r['Label'], r['Category'],
r['E [ksi]'], r['Nu'], r['Density [k/ft³]'],
r['Therm. Coeff. [1e-5/°F]'], r['G [ksi]'])
for _, r in df.iterrows() if isinstance(r['Label'], str)}
1
Read, do not retype
The All Materials sheet is the single source. Category + Label is the key; the eight tab sheets stay as the audit trail against the screenshots.
2
Derive G, do not store it
22 of 28 RISA values satisfy G = E / 2(1+ν) within 0.1%; only aluminum's fixed 3,787.5 ksi differs, by 0.25% to 1.2%. Deriving removes one column that can drift.
3
Convert units once
Keep kip-inch internally or switch to kN-m at load time. Never mix inside a stiffness matrix. The Metric twin of this library is the same rows converted.
4
Separate analysis from design
E, G, ν, γ, α feed the solver. Fy, Fu, f'c, f'm, Ry, Rt feed a later code-check module.
5
Special cases
Concrete E from f'c; masonry weight from block and grout; wood E from an NDS lookup; RIGID as a constraint.

## Slide 14
Transcription checks and caveats
Python Solver Rev.2 | Material Library, Imperial | 14
Verified against the source
Concrete E values reproduce ACI 318 Eq. 19.2.2.1(a) to the nearest ksi for all six mixes.
Masonry E equals 900 f'm (concrete) and 700 f'm (clay) exactly.
Cold-formed G = 29,500 / 2.6 = 11,346 ksi. Hot-rolled G = 29,000 / 2.6 = 11,154 ksi.
22 of 28 tabulated G values agree with E / 2(1+ν) within 0.1%; aluminum's fixed 3,787.5 ksi (= 3E/8) is the exception.
Recorded as displayed, with a flag
Stainless SS1: SI magnitudes under ksi headers. Do not use until the unit basis is confirmed in RISA.
General RIGID: G is blank in RISA and left blank in the workbook.
gen_Alum (E 10,600, α 1.29) differs slightly from the Aluminum tab (10,100, 1.3). Both kept as shown.
Labels reconstructed where the screen cut them off
Wood rows 7 to 12 read "24F-1.8E DF..." and "LVL-PRL Co..." on screen. Full labels were rebuilt from the Species column (24F-1.8E DF_BAL, LVL-PRL 1.5E_2250F, and so on).
Aluminum row 6 reads "6061-T6..."; its strengths (Ftu 24, Fty 15 ksi) are the welded 6061-T6 values, so it is labelled 6061-T6 (welded).
What RISA_Materials_Library_Imperial.xlsx gives you
README with these notes.
One sheet per RISA tab, transcribed inputs in blue, formula check columns for G.
Masonry Self Weight dialog captured on the Masonry sheet.
All Materials: flat table of 41 rows, filterable.
Glossary: every column, its meaning and its use in the solver.
Twin file: RISA_Materials_Library_Metric.xlsx, same rows in MPa and kN/m³.

## Slide 15
Next steps for Rev.2
1
Load
Read All Materials into a Material dataclass; derive G; convert α.
2
Benchmark
Run the 6 m cube with A992 and Conc4000NW; compare deflections with RISA.
3
Extend
Add the concrete E rule, masonry wall weight, and an NDS wood lookup.
4
Resolve
Confirm the Stainless unit basis in RISA and update the row in both libraries.
Files in the Materials folder: RISA_Materials_Library_Imperial.xlsx and this deck, with the Metric twin alongside. Source screenshots remain the authority.