## Slide 1
Material Library
Standard Metric units
The RISA-3D material tables as the reference for Python Solver Rev.2
Eight material tabs, 41 materials, one masonry self-weight rule, in MPa, kN/m³ and °C. Converted from the RISA Imperial display with 1 ksi = 6.894757 MPa and 1 k/ft³ = 157.0875 kN/m³. What every column means, how the numbers were derived, and how the solver should consume them.
Mark Airol Escranda | Numerical Methods, Lab 03 | September 2026
Notes: Source: nine screenshots in the Materials folder. Companion workbook: RISA_Materials_Library_Metric.xlsx.

## Slide 2
Where material properties enter the solver
Python Solver Rev.2 | Material Library, Standard Metric | 2
A stiffness solver never uses a material name. It uses four numbers, and a fifth for loads. Everything on the eight RISA tabs exists to supply these.
E
Modulus of elasticity
Axial term EA/L and bending terms 12EI/L³, 6EI/L², 4EI/L in the member stiffness matrix. Also plate membrane stiffness.
G
Shear modulus
Torsional stiffness GJ/L, and the shear-deformation correction on deep members. Isotropic rule: G = E / 2(1+ν).
ν
Poisson's ratio
Links G to E and sets the in-plane coupling of plate and shell elements.
γ
Unit weight
Self-weight load: w = γ · A per unit length. Converted to nodal forces in the load vector.
α
Thermal coefficient
Thermal strain α·ΔT, turned into equivalent member end forces for temperature load cases.
Strengths (Fy, Fu, f'c, f'm, Ftu) do not change the stiffness solution. They belong to the design-check layer that sits on top of the analysis.

## Slide 3
The library at a glance
Python Solver Rev.2 | Material Library, Standard Metric | 3
8
material tabs in RISA-3D
41
materials transcribed
5
stiffness properties shared by every tab
Tab | Rows | What it holds | Extra columns beyond the shared five
Hot Rolled | 5 | A36, A572, A992, A500 steels | Yield, Fu, Ry, Rt
Cold Formed | 2 | A570_33, A607_C1_55 | Yield, Fu
Wood | 12 | Solid sawn, glulam, LVL | Type, Database, Species, Grade, Cm, Ci, Emod
Concrete | 6 | 20.7 to 27.6 MPa, normal and lightweight | f'c, Lambda, Flex Steel, Shear Steel
Masonry | 2 | Concrete and clay masonry | f'm, Flex Steel, Shear Steel, Self Weight rule
Aluminum | 6 | 3003, 5052, 6061, 6063 alloys | Table B.4, kt, Ftu, Fty, Fcy, Fsu, Ct
Stainless | 1 | SS1 | n (Ramberg-Osgood), Yield, Fu
General | 7 | Generic concrete, aluminum, steel, RIGID | Plate Methodology

## Slide 4
The five shared columns, and their units
Python Solver Rev.2 | Material Library, Standard Metric | 4
Column | Unit | Meaning | Solver note
E [MPa] | N/mm² | Modulus of elasticity | 1 MPa = 0.1450377 ksi. Steel 199,948 MPa = 29,000 ksi (codes round to 200 GPa).
G [MPa] | N/mm² | Shear modulus | Derive from E and ν when blank; tabulated G agrees within 0.1% on 22 of 28 rows.
Nu | dimensionless | Poisson's ratio | Steel 0.30, concrete 0.15, masonry 0.25, aluminum 0.33, wood 0.30.
Therm. Coeff. [1e-6/°C] | 10⁻⁶ per °C | Coefficient of thermal expansion | Multiply by 1e-6 first: steel 11.7 → 11.7e-6 /°C (= 6.5e-6 /°F).
Density [kN/m³] | kN/m³ | Unit weight for self-weight | Mass density kg/m³ = kN/m³ × 1000 / 9.80665. Steel 76.97 kN/m³ = 7,849 kg/m³.
Unit strategy for the solver
This library is the Standard Metric twin of the Imperial one: every value converted from the RISA display with factors derived from 1 in = 25.4 mm and 1 lbf = 4.4482216152605 N. Work in kN and m internally (E in kPa) or N and mm (E in MPa), never a mixture.
A mixed-unit row is the classic silent error; the Stainless tab shows what that looks like.
Consistency check built into the workbook
Every tab with a G column carries a formula column: G_calc = E / 2(1+ν), and the percentage difference from the tabulated G.
22 of the 28 rows with a G value agree within 0.1%. The six aluminum rows carry a fixed 26,114 MPa, which is 3E/8 with E = 69,637 (ν = 1/3 exactly), so they sit 0.25% off, and 1.2% off for 5052 with its E of 70,327.

## Slide 5
Hot Rolled steel
Python Solver Rev.2 | Material Library, Standard Metric | 5
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | Yield [MPa] | Ry | Fu [MPa] | Rt
A36 Gr.36 | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | 248.2 | 1.5 | 399.9 | 1.2
A572 Gr.50 | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | 344.7 | 1.1 | 399.9 | 1.2
A992 | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | 344.7 | 1.1 | 399.9 | 1.2
A500 Gr.42 | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | 289.6 | 1.3 | 399.9 | 1.1
A500 Gr.46 | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | 317.2 | 1.2 | 399.9 | 1.1
Converted from Materials-SS-Hot-Rolled-TAB.png
Five ASTM grades. Stiffness is identical across all of them: E = 199,948 MPa (200 GPa), G = 76,904 MPa, ν = 0.30, γ = 76.97 kN/m³.
Only the strength columns differ. A36 yields at 248.2 MPa; A572 Gr.50 and A992 at 344.7 MPa (NSCP Grade 345); A500 tube steels at 289.6 and 317.2 MPa. Fu is 399.9 MPa throughout.
Ry and Rt are the AISC 341 expected-strength ratios. Ry × Fy is the expected yield (A36: 1.5 × 248.2 = 372 MPa), used when a seismic design must guarantee that a brace or link yields before its connection.
For the solver: one stiffness set, five design labels. The material dictionary can share E, G, ν and vary only Fy, Fu, Ry, Rt.
Unit weight check
76.97 kN/m³ ÷ 9.80665 × 1000 = 7,849 kg/m³, the handbook 7,850 kg/m³ of structural steel. A W310×39 (A = 4,930 mm²) weighs 76.97 × 4,930e-6 = 0.379 kN/m = 38.7 kg/m, matching its designation.

## Slide 6
Cold Formed steel
Python Solver Rev.2 | Material Library, Standard Metric | 6
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | Yield [MPa] | Fu [MPa]
A570_33 | 203,395 | 78,228 | 0.3 | 11.7 | 76.97 | 227.5 | 358.5
A607_C1_55 | 203,395 | 78,228 | 0.3 | 11.7 | 76.97 | 379.2 | 482.6
Converted from Materials-SS-Cold-Formed-TAB.png
Two sheet-steel grades used for light-gauge framing: A570 Gr.33 (Fy 227.5, Fu 358.5 MPa) and A607 Class 1 Gr.55 (Fy 379.2, Fu 482.6 MPa).
Note the different modulus: E = 203,395 MPa, not 199,948. AISI S100 specifies 29,500 ksi (203.4 GPa) for cold-formed members, and G = 78,228 MPa follows from E / 2(1.3).
No Ry or Rt columns. Cold-formed design under AISI does not use the AISC expected-strength factors.
For the solver: keep this tab separate from Hot Rolled even though the numbers look alike. A 1.7% difference in E is real and shows up in deflections.
Why 203,395 matters
Deflection is proportional to 1/E, so swapping in 200,000 MPa overstates cold-formed deflection by 1.7%. Small, but it is the kind of drift that makes a solver disagree with RISA on a benchmark.

## Slide 7
Concrete
Python Solver Rev.2 | Material Library, Standard Metric | 7
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | f'c [MPa] | Lambda | Flex Steel [MPa] | Shear Steel [MPa]
Conc3000NW | 21,760 | 9,460 | 0.15 | 10.8 | 22.78 | 20.7 | 1 | 413.7 | 413.7
Conc3500NW | 23,504 | 10,218 | 0.15 | 10.8 | 22.78 | 24.1 | 1 | 413.7 | 413.7
Conc4000NW | 25,124 | 10,921 | 0.15 | 10.8 | 22.78 | 27.6 | 1 | 413.7 | 413.7
Conc3000LW | 14,376 | 6,254 | 0.15 | 10.8 | 17.28 | 20.7 | 0.75 | 413.7 | 413.7
Conc3500LW | 15,527 | 6,750 | 0.15 | 10.8 | 17.28 | 24.1 | 0.75 | 413.7 | 413.7
Conc4000LW | 16,603 | 7,219 | 0.15 | 10.8 | 17.28 | 27.6 | 0.75 | 413.7 | 413.7
Converted from Materials-SS-Concrete-TAB.png
Six mixes: f'c = 20.7, 24.1 and 27.6 MPa (3,000 to 4,000 psi), each in normal weight (22.78 kN/m³, λ = 1.0) and lightweight (17.28 kN/m³, λ = 0.75).
E is not typed in; it is derived from f'c and density with ACI 318 / NSCP Eq. 19.2.2.1(a) in SI: Ec = 0.043 · wc¹·⁵ · √f'c, with wc in kg/m³ and f'c in MPa.
Check: 0.043 × 2323¹·⁵ × √20.7 = 21,900 MPa against 21,760 tabulated; the 0.6% gap is the rounding of 0.043 (exact: 0.0428). Lightweight: 0.043 × 1762¹·⁵ × √20.7 = 14,470 vs 14,376.
ν = 0.15 for all mixes, so G = E / 2.3. Flex Steel and Shear Steel (413.7 MPa) are the Grade 60 rebar yield, NSCP Grade 420, used by the design layer only.
Rule for the solver
Store f'c and γ as the inputs and compute E on load. To reproduce RISA exactly, convert to Imperial, apply E = wc^1.5 × 33 × √f'c (psi), and convert back; the SI 0.043 coefficient alone lands 0.6% high.

## Slide 8
Masonry, and how its self-weight is computed
Python Solver Rev.2 | Material Library, Standard Metric | 8
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | Self Weight [kN/m³] | f'm [MPa] | Flex Steel [MPa] | Shear Steel [MPa]
Concrete Matl | 9,308 | 3,723 | 0.25 | 10.8 | Custom | 10.3 | 413.7 | 413.7
Clay Matl | 7,239 | 2,896 | 0.25 | 10.8 | Custom | 10.3 | 413.7 | 413.7
Converted from Materials-SS-Masonry-TAB.png
Masonry-Self-Weight-WND.png
Self Weight = Custom
The tab does not carry a density. Instead the dialog selects "Using Block and Grout Properties": block material 115 pcf (18.07 kN/m³), grout 140 pcf (21.99 kN/m³).
Wall weight then depends on block thickness and grout spacing. The greyed-out alternative is a uniform 12.57 kN/m³ (80 pcf).
Two assemblies: concrete masonry (E 9,308 MPa) and clay masonry (E 7,239 MPa), both with f'm = 10.3 MPa and ν = 0.25.
E follows TMS 402: Em = 900 f'm for concrete masonry (900 × 10.34 = 9,308) and 700 f'm for clay (700 × 10.34 = 7,239). G = 0.4 Em = 3,723 and 2,896 MPa, which also equals E / 2(1.25).
For the solver: masonry needs a wall-panel weight routine, not a scalar density. Simplest faithful implementation: weight per area = f(block thickness, block density, grout density, grout spacing) from the NCMA tables, with 12.57 kN/m³ as the fallback.

## Slide 9
Wood
Python Solver Rev.2 | Material Library, Standard Metric | 9
Label | Type | Species | Grade | α [1e-6/°C] | γ [kN/m³]
DF/SPine | Solid Sawn | Com Species Group I DF,SP | No.1 | 5.4 | 5.5
HF/Spruce Fir | Solid Sawn | Com Species Group II HF,SPF | No.1 | 5.4 | 5.5
DF | Solid Sawn | Douglas Fir-Larch | No.1 | 5.4 | 5.5
SP | Solid Sawn | Southern Pine | No.1 | 5.4 | 5.5
HF | Solid Sawn | Hem-Fir | No.1 | 5.4 | 5.5
SPF | Solid Sawn | Spruce-Pine-fir | No.1 | 5.4 | 5.5
24F-1.8E DF_BAL | Glulam | 24F-1.8E_DF_BAL | na | 5.4 | 5.5
24F-1.8E DF_UNBAL | Glulam | 24F-1.8E_DF_UNBAL | na | 5.4 | 5.5
24F-1.8E SP_BAL | Glulam | 24F-1.8E_SP_BAL | na | 5.4 | 5.5
24F-1.8E SP_UNBAL | Glulam | 24F-1.8E_SP_UNBAL | na | 5.4 | 5.5
LVL-PRL 1.5E_2250F | Custom | LVL_PRL_1.5E_2250F | na | 5.4 | 5.5
LVL-PRL 2.0E_2900F | Custom | LVL_PRL_2.0E_2900F | na | 5.4 | 5.5
Converted from Materials-SS-Wood-TAB.png (labels in rows 7 to 12 truncated on screen; reconstructed from Species)
Twelve entries in three families: six visually graded solid-sawn species (No.1), four 24F-1.8E glulam layups from NDS Table 5A (balanced and unbalanced, DF and SP), and two custom LVL products (1.5E-2250F, 2.0E-2900F).
This tab stores keys, not stiffness. E, Fb, Fv and Fc are looked up in the NDS Supplement by Type, Database, Species and Grade; Emod (1.0) scales the tabulated E, and Cm / Ci apply wet-service and incising factors when checked (none are).
Shared values: ν = 0.30, α = 5.4 × 1e-6 /°C, γ = 5.50 kN/m³ (561 kg/m³).
For the solver: wood needs a lookup layer. Until the NDS table is loaded, a placeholder E (for example 11,700 MPa for No.1 DF-L) keeps the model solvable.
The glulam label decoded
24F-1.8E: allowable bending stress 2,400 psi (16.5 MPa) and E = 1.8 × 10⁶ psi = 12,411 MPa. BAL and UNBAL mark balanced or unbalanced layups; DF and SP are Douglas Fir and Southern Pine laminations.

## Slide 10
Aluminum
Python Solver Rev.2 | Material Library, Standard Metric | 10
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | Ftu [MPa] | Fty [MPa] | Fcy [MPa] | Fsu [MPa]
3003-H14 | 69,637 | 26,114 | 0.33 | 23.4 | 27.18 | 131 | 110.3 | 89.6 | 82.7
6061-T6 | 69,637 | 26,114 | 0.33 | 23.4 | 27.18 | 262 | 241.3 | 241.3 | 165.5
6063-T5 | 69,637 | 26,114 | 0.33 | 23.4 | 27.18 | 151.7 | 110.3 | 110.3 | 89.6
6063-T6 | 69,637 | 26,114 | 0.33 | 23.4 | 27.18 | 206.8 | 172.4 | 172.4 | 131
5052-H34 | 70,327 | 26,114 | 0.33 | 23.4 | 27.18 | 234.4 | 179.3 | 165.5 | 137.9
6061-T6 (welded) | 69,637 | 26,114 | 0.33 | 23.4 | 27.18 | 165.5 | 103.4 | 103.4 | 103.4
Converted from Materials-SS-Aluminum-TAB.png (row 6 truncated on screen; strengths match welded 6061-T6)
Six alloy-tempers: 3003-H14, 5052-H34, 6061-T6 (plain and welded), 6063-T5 and 6063-T6.
Stiffness is nearly constant: E = 69,637 MPa (70,327 for 5052), G = 26,114 MPa for every row (3E/8, the ADM value for ν = 1/3), ν = 0.33, γ = 27.18 kN/m³ (2,771 kg/m³), α = 23.4 × 1e-6 /°C, twice that of steel.
Strength columns follow the Aluminum Design Manual: Ftu, Fty (tension), Fcy (compression), Fsu (shear), with kt = 1.0 and the buckling constants taken from Table B.4-1 or B.4-2 depending on temper. Ct = 141 is the compression constant.
Welding halves the strength but not the stiffness: 6061-T6 drops from Fty 241.3 to 103.4 MPa in the welded row while E stays at 69,637 MPa.
Thermal note for the solver
Aluminum expands at 23.4e-6 /°C versus 11.7e-6 for steel. A 12 m aluminum member under a 33 °C rise grows 9.3 mm; the same steel member grows 4.6 mm. Thermal load cases must read α per material, not a global constant.

## Slide 11
Stainless: one row, and a unit trap
Python Solver Rev.2 | Material Library, Standard Metric | 11
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | n | Yield [MPa] | Fu [MPa]
SS1 | 193,100 | 74,325.48 | 0.3 | 1.674 | 8.009 | 5.6 | 206.84 | 517.11
Converted from Materials-SS-Stainless-TAB.png (carried over unconverted)
Column | Displayed in RISA | If read as ksi | If read as MPa
E | 1.931e+5 | 193,100 ksi (6.7× steel) | 193,100 MPa = 28,000 ksi
Yield | 206.843 | 206.8 ksi | 206.843 MPa = 30.0 ksi
Fu | 517.107 | 517.1 ksi | 517.107 MPa = 75.0 ksi
Density | 8.009 | 8,009 pcf | 8.0 g/cm³ (specific gravity of stainless)
SS1 is the only stainless entry. In RISA its values sit under ksi headers but are SI magnitudes: 30 ksi yield and 75 ksi ultimate are the textbook Type 304 values, and 193 GPa is its modulus.
This Metric library therefore carries the row over unconverted (E 193,100 MPa, Fy 206.8 MPa, Fu 517.1 MPa). Density 8.009 and thermal 1.674 are kept as displayed; the likely readings are 8.0 g/cm³ (78.5 kN/m³) and 16.7e-6 /°C.
n = 5.6 is the Ramberg-Osgood exponent, the one property unique to this tab. Stainless has no sharp yield, so RISA models the stress-strain curve as ε = σ/E + 0.002 (σ/Fy)ⁿ.
Treat this row as a caution, not a value, until the unit basis is confirmed in RISA. The workbook flags it on the Stainless and All Materials sheets.

## Slide 12
General materials and the RIGID link
Python Solver Rev.2 | Material Library, Standard Metric | 12
Label | E [MPa] | G [MPa] | Nu | α [1e-6/°C] | γ [kN/m³] | Plate Methodology
gen_Conc3NW | 21,753 | 9,460 | 0.15 | 10.8 | 22.78 | Isotropic
gen_Conc4NW | 25,124 | 10,921 | 0.15 | 10.8 | 22.78 | Isotropic
gen_Conc3LW | 14,376 | 6,247 | 0.15 | 10.8 | 17.28 | Isotropic
gen_Conc4LW | 16,603 | 7,219 | 0.15 | 10.8 | 17.28 | Isotropic
gen_Alum | 73,084 | 28,110 | 0.3 | 23.2 | 27.18 | Isotropic
gen_Steel | 199,948 | 76,904 | 0.3 | 11.7 | 76.97 | Isotropic
RIGID | 6,894,757 |  | 0.3 | 0 | 0 | Isotropic
Converted from Materials-SS-General-TAB.png
Seven generic entries for plates, solids and quick models: four concretes (20.7 and 27.6 MPa, normal and lightweight), one aluminum, one steel, and RIGID.
gen_Conc3NW (E 21,753) and gen_Conc4NW (E 25,124) mirror the Concrete tab values within 7 MPa; gen_Alum uses E 73,084 MPa and α 23.2, slightly different from the Aluminum tab.
Plate Methodology = Isotropic for every entry: the same E in every in-plane direction, which is what the solver's plate stiffness should assume.
RIGID has E = 6,894,757 MPa (1e+6 ksi), no G, and zero density and thermal coefficient. It is a modeling device for stiff links and rigid offsets, not a real material.
Handling RIGID in the solver
Do not simply use E = 6.9e6 MPa in the stiffness matrix; a 34:1 stiffness ratio to steel is fine, but combine it with tiny members and the matrix becomes ill-conditioned. Better: implement rigid links as constraint equations, or cap E at 1,000× the stiffest real material.

## Slide 13
How Solver Rev.2 should consume the library
Python Solver Rev.2 | Material Library, Standard Metric | 13
from dataclasses import dataclass
import pandas as pd
@dataclass
class Material:
label: str; category: str
E: float; nu: float; density: float
alpha: float; G: float | None = None
Fy: float | None = None; Fu: float | None = None
def __post_init__(self):
if self.G is None: # isotropic rule
self.G = self.E / (2 * (1 + self.nu))
self.alpha *= 1e-6 # library stores 1e-6/degC
df = pd.read_excel('RISA_Materials_Library_Metric.xlsx',
sheet_name='All Materials', header=3)
LIB = {r['Label']: Material(r['Label'], r['Category'],
r['E [MPa]'], r['Nu'], r['Density [kN/m³]'],
r['Therm. Coeff. [1e-6/°C]'], r['G [MPa]'])
for _, r in df.iterrows() if isinstance(r['Label'], str)}
1
Read, do not retype
The All Materials sheet is the single source. Category + Label is the key; the eight tab sheets stay as the audit trail against the screenshots.
2
Derive G, do not store it
22 of 28 RISA values satisfy G = E / 2(1+ν) within 0.1%; only aluminum's fixed 26,114 MPa differs, by 0.25% to 1.2%. Deriving removes one column that can drift.
3
Convert units once
Keep N-mm (E in MPa) or kN-m (E in kPa) internally. Never mix inside a stiffness matrix. The Imperial twin of this library is the RISA original.
4
Separate analysis from design
E, G, ν, γ, α feed the solver. Fy, Fu, f'c, f'm, Ry, Rt feed a later code-check module.
5
Special cases
Concrete E from f'c; masonry weight from block and grout; wood E from an NDS lookup; RIGID as a constraint.

## Slide 14
Transcription checks and caveats
Python Solver Rev.2 | Material Library, Standard Metric | 14
Verified against the source
Concrete E values reproduce ACI 318 Eq. 19.2.2.1(a) (Imperial form) to the nearest ksi for all six mixes.
Masonry E equals 900 f'm (concrete) and 700 f'm (clay) exactly.
Cold-formed G = 203,395 / 2.6 = 78,229 MPa. Hot-rolled G = 199,948 / 2.6 = 76,903 MPa.
22 of 28 tabulated G values agree with E / 2(1+ν) within 0.1%; aluminum's fixed 26,114 MPa (= 3E/8) is the exception.
Recorded as displayed, with a flag
Stainless SS1: carried over unconverted because the RISA display is already SI. Density and thermal kept as displayed; confirm before use.
General RIGID: G is blank in RISA and left blank in the workbook.
gen_Alum (E 73,084, α 23.2) differs slightly from the Aluminum tab (69,637, 23.4). Both kept as converted.
Labels reconstructed where the screen cut them off
Wood rows 7 to 12 read "24F-1.8E DF..." and "LVL-PRL Co..." on screen. Full labels were rebuilt from the Species column (24F-1.8E DF_BAL, LVL-PRL 1.5E_2250F, and so on).
Aluminum row 6 reads "6061-T6..."; its strengths (Ftu 24, Fty 15 ksi) are the welded 6061-T6 values, so it is labelled 6061-T6 (welded).
What RISA_Materials_Library_Metric.xlsx gives you
README with the conversion basis and these notes.
One sheet per RISA tab in MPa, kN/m³ and 1e-6/°C, formula check columns for G.
Masonry Self Weight dialog captured on the Masonry sheet.
All Materials: flat table of 41 rows with mass density in kg/m³ by formula, filterable.
Glossary: every column, its meaning and its use in the solver.
Twin file: RISA_Materials_Library_Imperial.xlsx, the RISA original.

## Slide 15
Next steps for Rev.2
1
Load
Read All Materials into a Material dataclass; derive G; convert α.
2
Benchmark
Run the 6 m cube with A992 and Conc4000NW; compare deflections with RISA.
3
Extend
Add the concrete E rule, masonry wall weight, and an NDS wood lookup.
4
Resolve
Confirm the Stainless unit basis in RISA and update the row in both libraries.
Files in the Materials folder: RISA_Materials_Library_Metric.xlsx and this deck, with the Imperial twin alongside. Source screenshots remain the authority.