## Slide 1
Units
Imperial and Standard Metric for Python Solver Rev.2
What RISA and STAAD mean by each unit set, the exact definitions every conversion rests on, the material library in both systems, and the rule that keeps a stiffness matrix consistent.
Mark Airol Escranda | Numerical Methods, Lab 03 | September 2026
Notes: Companion workbook: Units_Imperial_Metric.xlsx. All factors there are formulas built from 1 in = 25.4 mm, 1 lbf = 4.4482216152605 N, g = 9.80665 m/s².

## Slide 2
A solver is only as right as its units
Python Solver Rev.2 | Units | 2
The stiffness method is unit-blind: it multiplies whatever numbers it is handed. Consistency is the only rule, and every unit error is silent until a deflection looks absurd.
The rule
Pick one force unit F and one length unit L. Then E is F/L², A is L², I is L⁴, loads are F or F/L, and every stiffness term (EA/L, EI/L³, GJ/L) comes out in F/L or F·L/rad without any factor inside the matrix.
What RISA does
Displays any unit set you like but stores one internally and converts at the boundary. The Materials tabs show ksi and k/ft³ because the model was in the Imperial set. Switch the set and the same numbers appear as MPa and kN/m³.
What went wrong once
The Stainless SS1 row in this library reads 193,100 under a ksi header. It is 193,100 MPa. Used as ksi it would make stainless 6.7 times stiffer than steel and every deflection 85% too small.
The two sets used in practice: Imperial (kip, in, ft, ksi, °F), the RISA default and the one the Materials screenshots use; and Standard Metric (kN, m, mm, MPa, °C), the set NSCP and ASEP tables use in the Philippines.

## Slide 3
The two unit sets, quantity by quantity
Python Solver Rev.2 | Units | 3
Quantity | Imperial (RISA default) | Standard Metric (SI) | Solver internal | Watch for
Node coordinates | ft | m | L | RISA mixes ft for geometry, in for sections
Section dimensions | in | mm | L | AISC tables in in, ASEP tables in mm
Area / inertia | in² / in⁴ | mm² / mm⁴ | L² / L⁴ | 1 in⁴ = 416,231 mm⁴
Force | kip | kN | F | 1 kip = 4.448 kN
Moment | kip·ft | kN·m | F·L | STAAD may report kip·in
Stress, modulus | ksi | MPa = N/mm² | F/L² | kN and mm give kN/mm² = GPa; ×1000 for MPa
Distributed load | kip/ft | kN/m | F/L | 
Unit weight | k/ft³ | kN/m³ | F/L³ | SI tables often give kg/m³; multiply by g
Temperature change | °F | °C | ΔT | Coefficient must match the ΔT unit
Thermal coefficient | 1e-5 /°F | 1e-6 /°C | 1/ΔT | RISA stores the mantissa only
Deflection | in | mm | L | 
Spring stiffness | kip/in, kip·ft/rad | kN/m, kN·m/rad | F/L, F·L/rad | 

## Slide 4
Three exact definitions, and everything follows
Python Solver Rev.2 | Units | 4
Every conversion factor in the workbook is a formula built from these three constants. None of the derived factors is typed in, so none can be mistyped.
1 in
= 25.4 mm
exact, since 1959
1 lbf
= 4.448222 N
exact: 4.4482216152605 N = 0.45359237 kg × g
g
= 9.80665 m/s²
standard gravity, exact by convention
Derived factor | Built from | Value
ksi → MPa | 4448.2216 N / 25.4² mm² | 6.894757
kip → kN | 4.4482216 × 1000 / 1000 | 4.448222
kip·ft → kN·m | 4.448222 × 0.3048 | 1.355818
kip/ft → kN/m | 4.448222 / 0.3048 | 14.593903
k/ft³ → kN/m³ | 4.448222 / 0.3048³ | 157.087464
k/ft³ → kg/m³ | 157,087 N/m³ / 9.80665 | 16,018.46
in⁴ → mm⁴ | 25.4⁴ | 416,231.43
1e-5/°F → 1e-6/°C | × 1.8 × 10 | 18

## Slide 5
E and G in both systems
Python Solver Rev.2 | Units | 5
Material | E [ksi] | E [MPa] | E [GPa] | G [ksi] | G [MPa] | ν
A36 / A992 steel | 29,000 | 199,948 | 199.9 | 11,154 | 76,904 | 0.30
Cold-formed steel | 29,500 | 203,395 | 203.4 | 11,346 | 78,228 | 0.30
Conc4000NW | 3,644 | 25,124 | 25.1 | 1,584 | 10,921 | 0.15
Conc3000NW | 3,156 | 21,760 | 21.8 | 1,372 | 9,460 | 0.15
Concrete masonry | 1,350 | 9,308 | 9.3 | 540 | 3,723 | 0.25
6061-T6 aluminum | 10,100 | 69,637 | 69.6 | 3,787.5 | 26,114 | 0.33
Wood (24F-1.8E glulam) | 1,800 | 12,411 | 12.4 | n/a | n/a | 0.30
Why 200 GPa and 29,000 ksi are not the same number
29,000 ksi converts to 199,948 MPa. Codes round to 200,000 MPa (NSCP, Eurocode) and to 29,000 ksi (AISC). The 0.03% gap is harmless, but a solver benchmarked against RISA in Imperial should use 29,000 and convert, not 200,000.
The kN-mm trap
With F = kN and L = mm, stress comes out in kN/mm², which is GPa. Steel E is then 199.9, not 199,948. Choose kN and m (E in kPa: 199,948,000) or N and mm (E in MPa: 199,948) and stay there.

## Slide 6
Density: unit weight versus mass density
Python Solver Rev.2 | Units | 6
Material | RISA [k/ft³] | pcf | kN/m³ | kg/m³
Steel | 0.49 | 490 | 76.97 | 7,849
Normal-weight concrete | 0.145 | 145 | 22.78 | 2,323
Lightweight concrete | 0.11 | 110 | 17.28 | 1,762
Aluminum | 0.173 | 173 | 27.18 | 2,771
Wood | 0.035 | 35 | 5.50 | 561
Masonry (uniform alternative) | 0.08 | 80 | 12.57 | 1,281
Imperial tables give unit weight, a force per volume. SI tables usually give mass density in kg/m³. They differ by g: kN/m³ = kg/m³ × 9.80665 / 1000.
Steel is the check value: 490 pcf = 76.97 kN/m³ = 7,849 kg/m³, close to the 7,850 kg/m³ most SI handbooks quote.
Self-weight in the solver is w = γ·A. With γ in kN/m³ and A in mm², convert A to m² (÷ 1e6) or the load will be a million times too large.
Masonry has no scalar density in RISA (block and grout rule). The 0.08 k/ft³ shown is the uniform-density alternative that was not selected.
Formula behind the kg/m³ column
kg/m³ = (k/ft³ × 4448.2216 / 0.3048³) / 9.80665. For steel: 0.49 × 16,018.46 = 7,849. The workbook derives 16,018.46 from the three exact constants rather than storing it.

## Slide 7
Thermal coefficients: the mantissa trap
Python Solver Rev.2 | Units | 7
Material | RISA [1e-5/°F] | /°F | /°C | [1e-6/°C]
Steel | 0.65 | 6.5e-6 | 11.7e-6 | 11.7
Concrete, masonry | 0.6 | 6.0e-6 | 10.8e-6 | 10.8
Aluminum | 1.3 | 13.0e-6 | 23.4e-6 | 23.4
Wood | 0.3 | 3.0e-6 | 5.4e-6 | 5.4
gen_Alum (General tab) | 1.29 | 12.9e-6 | 23.2e-6 | 23.2
RISA's column header carries the exponent: the cell 0.65 means 0.65 × 1e-5 per °F. Read the number without the header and steel expands 100,000 times too fast.
A degree Celsius is a bigger step than a degree Fahrenheit, so the coefficient per °C is 1.8 times the coefficient per °F. Going from 1e-5/°F to 1e-6/°C is therefore × 18.
Check value: steel 11.7e-6 /°C is the figure in Eurocode 3 (12e-6) and AISC (6.5e-6 /°F) to within rounding.
Temperature itself is an offset conversion, °C = (°F − 32)/1.8, but temperature change is a pure factor, ΔT°C = ΔT°F / 1.8. Thermal loads use the change.
Worked example
A 6 m steel member warmed by 20 °C: ε = 11.7e-6 × 20 = 234e-6; ΔL = 234e-6 × 6000 mm = 1.40 mm. In Imperial: 6.5e-6 × 36 °F × 236.2 in = 0.055 in = 1.40 mm. Both routes must agree, and this is a good unit test for the solver.

## Slide 8
The material library in both systems
Python Solver Rev.2 | Units | 8
Representative rows from the Materials (Imperial) and Materials (Metric) sheets. The Metric sheet is entirely formula-driven from the Imperial sheet.
Label | E [ksi] | E [MPa] | γ [k/ft³] | γ [kN/m³] | Strength [ksi] | Strength [MPa] | Fu [ksi] | Fu [MPa]
A36 Gr.36 | 29,000 | 199,948 | 0.49 | 76.97 | 36 | 248.2 | 58 | 399.9
A992 | 29,000 | 199,948 | 0.49 | 76.97 | 50 | 344.7 | 58 | 399.9
A570_33 (cold formed) | 29,500 | 203,395 | 0.49 | 76.97 | 33 | 227.5 | 52 | 358.5
Conc3000NW | 3,156 | 21,760 | 0.145 | 22.78 | 3 (f'c) | 20.7 |  | 
Conc4000NW | 3,644 | 25,124 | 0.145 | 22.78 | 4 (f'c) | 27.6 |  | 
Concrete Matl (masonry) | 1,350 | 9,308 | Custom | Custom | 1.5 (f'm) | 10.3 |  | 
6061-T6 | 10,100 | 69,637 | 0.173 | 27.18 | 35 (Fty) | 241.3 | 38 (Ftu) | 262.0
DF (No.1, solid sawn) | NDS lookup | NDS lookup | 0.035 | 5.50 |  |  |  | 
Grade 60 rebar (Flex Steel and Shear Steel, 60 ksi) is 413.7 MPa, which is why NSCP calls it Grade 420. A992's 50 ksi is 344.7 MPa, sold locally as Grade 345.

## Slide 9
Unit strategy for Solver Rev.2
Python Solver Rev.2 | Units | 9
# Exact definitions: everything else derives from these
IN_MM, LBF_N, G0 = 25.4, 4.4482216152605, 9.80665
KSI_MPA = LBF_N * 1000 / IN_MM**2 # 6.894757
KIP_KN = LBF_N # 4.448222
KCF_KNM3 = LBF_N * 1000 / (IN_MM*12/1000)**3 # 157.0875
FT_M, IN4_MM4 = IN_MM*12/1000, IN_MM**4
class Units:
"""Solver works in kN and m internally (E in kPa)."""
@staticmethod
def from_imperial(E_ksi, dens_kcf, alpha_1e5F):
return dict(E=E_ksi*KSI_MPA*1000, # kPa
gamma=dens_kcf*KCF_KNM3, # kN/m3
alpha=alpha_1e5F*1e-5*1.8) # /degC
@staticmethod
def from_metric(E_MPa, gamma_kNm3, alpha_perC):
return dict(E=E_MPa*1000, gamma=gamma_kNm3,
alpha=alpha_perC)
# Geometry: ft -> m, in -> m, in^4 -> m^4 at input; m -> mm at output
1
One internal set
kN and m throughout: E in kPa, A in m², I in m⁴, loads in kN and kN/m. No factor ever appears inside the stiffness assembly.
2
Convert at the boundary
Input readers translate from Imperial or Metric into the internal set; output writers translate back to whichever set the user chose.
3
Derive factors, never type them
Three constants, everything else computed. The workbook and the code share the same derivation, so they cannot disagree.
4
Test both routes
The 6 m cube benchmark run in Imperial and in Metric must give the same deflections to floating-point precision.
5
Flag suspicious rows
Warn when E is outside 1 to 250 GPa or γ outside 1 to 100 kN/m³. SS1 would trip this check immediately.

## Slide 10
Six ways units go wrong, and the check for each
Python Solver Rev.2 | Units | 10
1
kg/m³ used as kN/m³
Self-weight 102 times too large.
Check: Steel must be 77 kN/m³, not 7,850.
2
kN with mm
E reads 200 instead of 200,000.
Check: Deflections a thousand times too big.
3
Mantissa without exponent
α = 0.65 /°F instead of 6.5e-6.
Check: A 20 °F rise stretches steel by 13 ft per ft.
4
kip·in vs kip·ft
Moments off by 12.
Check: Compare one member moment against hand statics.
5
MPa in a ksi column
The SS1 row: E 6.7 times steel.
Check: Range check: E between 1 and 250 GPa.
6
Geometry in ft, sections in in
I/L³ off by 12³ = 1,728.
Check: Convert all lengths to one unit at input.

## Slide 11
What is in Units_Imperial_Metric.xlsx
Python Solver Rev.2 | Units | 11
Conversion Factors
Three exact constants in yellow cells; twenty derived factors as formulas, each with its reciprocal and its derivation spelled out.
Unit Systems
Sixteen quantities with the Imperial unit, the Metric unit, the solver's internal dimension, and what to watch for.
Materials (Imperial)
All 41 RISA materials as transcribed: E, G, ν, α, γ, strength and Fu in ksi, k/ft³ and 1e-5/°F.
Materials (Metric)
The same 41 rows in MPa, GPa, kN/m³, kg/m³ and 1e-6/°C. Every cell is a formula linked to the Imperial sheet.
Converter
Type an Imperial value on the left or a Metric value on the right; the other side computes. Temperature handled as an offset.

## Slide 12
Next steps
1
Adopt
Fix kN and m as the internal set in Rev.2 and move all conversions into one Units module.
2
Link
Point the material reader at Materials (Imperial) or Materials (Metric) by a single flag.
3
Test
Run the 6 m cube in both systems; assert identical deflections and reactions.
4
Guard
Add range checks on E, γ and α so a row like SS1 is caught at load time.
Files in the Materials folder: Units_Imperial_Metric.xlsx and this deck, alongside RISA_Materials_Library.xlsx and its deck.